## Slide 1: Light Fidelity (Li-Fi) in data communication

## Slide 2: Nowadays, the increase in traffic leads to an increase in accidents. Moreover, the accidents take place as the following vehicle doesn’t understand the behavior of another vehicle due to which the driver fails to act accordingly. But, these accidents can be avoided if the vehicle traveling ahead can be able to communicate its actions properly to the following vehicle. This paper focuses on one of the applications of Li-Fi i.e. vehicle to vehicle communication. It is the wireless transfer of data from one vehicle to another using Li-Fi technology. The goal of this type of communication is to prevent road accidents by allowing vehicles to send the position and speed data to one another. The received data can be used for further development in vehicle control and can avoid accidents by controlling the speed of the vehicle. Li-Fi uses rapid pulses of light to transmit the information wirelessly that cannot be detected by a human eye.
Abstract

## Slide 3: Introduction
What is Li-Fi?
Li-Fi stands for Light Fidelity and is a Visible Light Communications (VLC) system which uses light to send wireless data embedded in its beam.
A Li-Fi enabled device converts the beam of light into an electrical signal. The signal is then converted back into data.
The term was coined by German physicist Harald Haas during a TED Talk in 2011. He envisioned the idea of using light bulbs as wireless routers.
LiFi bulbs are outfitted with a chip that modulates the light imperceptibly for optical data transmission. LiFi data is transmitted by the household LED bulbs and received by photoreceptors.

## Slide 4: Architecture of Li-Fi system
Li-Fi which can be the future of data communication appears to be a fast and cheap optical version of Wi-Fi. It uses visible light of electromagnetic spectrum between 400 THz and 800 THz as optical carrier for data transmission and illumination.
The main components of a basic Li-Fi system are :
a) A high brightness white LED which acts as transmission source.
b) A silicon photodiode with good response to visible light as the receiving element.
Working
LED light bulbs can be dipped and dimmed,
up and down at extremely high speeds,
without being visible to the human eye.
The tiny changes/pulses in the rapid dimming
of LED bulbs is then converted by the ‘receiver’
into electrical signal. The signal is then converted
back into a binary data stream that we would
recognize as web, video and audio applications
that run on internet enabled devices.

## Slide 5: Areas of applications
Military-Li-Fi coverage can be limited to a small lit area such as a tent. Thus it can limit access to sensitive information under specific light and in areas where mobile phones can’t be used such as ammunition dumps.
Underwater Communication-Light can travel through water unlike Wi-Fi’s radio signals that will be swallowed up by the water. This way underwater vehicles communicate with one another.
Traffic Lights-The LED bulbs in traffic lights could provide drivers with weather conditions and traffic updates while they wait at a traffic light.
Security-Li-Fi has a shorter range than Wi-Fi and because of this, is more secure than Wi-Fi. This is because the shorter the range, the less chance of malicious interceptions within the data stream. This could be very useful in industries that handle large counts of sensitive data, for example healthcare.
Li-Fi Enabled Street Lights-Cities could definitely benefit from Li-Fi enabled street lights to provide internet access to mobile phones. This public internet access could make walking home at night safer and also help with tourism by providing an outlet for local information.

## Slide 6: Future of Li-Fi
“In two years time, you will see Li-Fi on the market on many levels,” says Deepak Solanki of , an Estonian company which is testing the technology in its offices.
Right now, Li-Fi is meant as a complimentary device to be used along with Wi-Fi, but in the future, Li-Fi will be the dominant internet connection device around. Li-Fi will become more secure than Wi-Fi.
A startup known as Velmenni is at the forefront of this technological revolution in India. There is certainty of development of future applications of the Li-Fi which can be extended to different platforms.
Lights will not only find a place on your study desks and your offices but also in a form of excellent wireless communication.

## Slide 7: Literature Survey in medical application
Title : li-fi based health monitoring system for infants
Author : Hasnain Ali, M. Ibtehaj Ahmad, Anoshah Malik
Working principle : This system is proposed for the infants to monitor health parameters like Heartbeat and Oxygen Level. MAX30100 used for the monitoring of Heartbeat and Oxygen Level of the infant. Here they propose a compact system that can be installed in the infant’s bag. This system comprises of wearable sensors and wearable microcontrollers for physical flexibility of the infants.

## Slide 8: continued
Title : Smart navigation with AI Engine for Li-Fi based Medical Indoor Environment
Author : Ho Kyung Yu, Jeong Gon Kim
Working principle : First, the location information is collected using Li-Fi, and then the user is guided through the location information data and the AI engine. In this paper, we use J-NERD as AI Engine and J-NERL as entity link model of J-NERD shows the process of guiding the user to the waiting time and route. When the user tells the LC device what user's symptoms are, the LC Device sends the information to the Central Server.

## Slide 9: Literature survey in vehicle to vehicle communication
Title : Li-Fi Based Automatic Traffic Signal Control for Emergency Vehicles
Author : Shanmughasundaram R, Prasanna Vadanan S, Vivek Dharmarajan
Working principle : when an emergency vehicle enters
into a congested lane it sends a message saying “emergency”.
If there is a non-emergency vehicle in front of it, the alert
message will be received by the transceiver of the
non-emergency vehicle. When it receives the alert message,
it informs the driver to move apart from the lane and
also informs traffic signal control.
The signal control, on receiving the alert
message, will turn green.

## Slide 10: continued
Title : Design and Implementation of a Vehicle to Vehicle Communication System Using Li-Fi Technology
Author : Noof Al Abdulsalam, Raya Al Hajri, Zahra Al Abri, Zainab Al Lawati, and Mohammed M. Bait-Suwailam
Working principle : This proposed system has 2 scenarios. First scenario- when vehicle 1 is braking, the speed meter in the vehicle will be sensing that the current speed is lower than the previous speed. Thus, a message will be sent through the transmitter which is placed in the rear lights to vehicle 2. The message will be received by vehicle 2 using the photodiode which is placed at the front of vehicle 2. A notice of (Slow DOWN) will be displayed in vehicle 2 using an LCD. Second scenario- when vehicle 1 is in T- junction, it will keep sending its speed-information to vehicle 2 using the LED at the headlights. The speed-information will be received by the photodiode in vehicle 2 and compared to vehicle 2 speed’s. If vehicle 2 is about to cross the junction while vehicle 1 is moving with a high speed, the driver will be alerted to check the other vehicle which is around in the area.

## Slide 11: continued
Title : Vehicle to Vehicle Communication Using RF and IR Technology
Author :Eftekhar Hossain, Nursadul Mamun , Md. Fahim Faisal
Working Principle : Both radio Frequency and infrared ray communication technique has been used in this
System. RF transmitter and IR transmitter are placed in front of the driver and both
receivers are placed behind the vehicle. Receivers are
attached with a PIC microcontroller which takes transmitted
signal that sends by the transmitters and read the signal to
reproduce the messages. A LCD is used to show the
receiving messages and a buzzer is also used to draw the
attention of driver. The circuit uses a RF transmitter and
receiver to send and receive messages to the left and right
side vehicle and uses a TSOP1738 IR receiver module at the
back side of the vehicle to receive the 38 kHz frequency IR
pulses from the IR transmitter which send message to the
front side vehicle.

## Slide 12: Literature survey on Load balancing using Li-Fi
Title : Optimization of Load Balancing in Hybrid LiFi/RF Networks
Author : Yunlu Wang, Dushyantha A. Basnayaka, Xiping Wu and Harald Haas
Working principle : In order to guarantee a quality of service (QoS) for all users in the network, a RF network is considered as an additional wireless networking layer. With regard to moving users, the hybrid LiFi/RF system dynamically allocates either a LiFi AP or a RF AP to users based on their channel state information (CSI). In this study, a dynamic load balancing scheme is proposed, which takes the handover overhead into account in order to improve the overall system throughput. Joint optimization algorithm (JOA) and separate optimization algorithm (SOA), which jointly and separately optimize the access point assignment and resource allocation respectively are proposed.

## Slide 13: Comparative study
Vehicle to vehicle communication |  |  | Medical application |  | Load Balancing
Using GSM | Using DSRC | Using RFID | For Infants | Navigation with AI Engine | 
Infrastructure needed to built in these communication systems is relatively high when compared to other protocols and also it requires high bandwidth. | 5.9 GHz DSRC - These radio frequency (RF) based communication system has some limitations i.e., interference, congested spectrum and security. These limitations can be overcome by using Visible Light Communication (VLC). It provides high bandwidth, security, interference immunity, and high data rate. | The main disadvantage of RFID is low security offered when the messages are prone to unauthorized access. Where as li-fi provides better security as compared to RFID. | MAX30100 used for the monitoring of Heartbeat and Oxygen Level of the infant. The system comprises of wearable sensors and wearable microcontrollers for physical flexibility of the infants. | The location information is collected using Li-Fi, and then the user is guided through the location information data and the AI engine. The system uses J-NERD as AI Engine and J-NERL as entity link model of J-NERD shows the process of guiding the user to the waiting time and route. When the user tells the LC device what user's symptoms are, the LC Device sends the information to the Central Server. | In order to guarantee a quality of service (QoS) for all users in the network, a RF network is considered as an additional wireless networking layer. With regard to moving users, the hybrid LiFi/RF system dynamically allocates either a LiFi AP or a RF AP to users based on their channel state information (CSI). The proposed takes the handover overhead into account in order to improve the overall system throughput. Joint optimization algorithm (JOA) and separate optimization algorithm (SOA), which jointly and separately optimize the access point assignment and resource allocation respectively are proposed.

## Slide 14: ADVANTAGES OF LIFI
Li-Fi can solve problems related to the insufficiency of radio frequency bandwidth because this technology uses Visible light spectrum that has still not been greatly utilized.
High data transmission rates of up to 10Gbps can be achieved.
Since light cannot penetrate walls, it provides privacy and security that Wi-Fi cannot.
Li-Fi has low implementation and maintenance costs.
Li-Fi has its advantages in electromagnetic sensitive areas such as aircraft cabins, hospitals, nuclear power plants without causing electromagnetic interference.
Transmission of data is faster and easy.

## Slide 15: Limitations of Li-Fi
Internet cannot be used without a light source. This could limit the locations and situations in which Li-Fi could be used.
Because it uses visible light, and light cannot penetrate walls, the signal's range is limited by physical barriers.
Other sources of light may interfere with the signal. One of the biggest potential drawbacks is the interception of signals outdoors. Sunlight will interfere the signals, resulting in interrupted Internet.
A whole new infrastructure for Li-Fi would need to be constructed.
High installation cost of the VLC systems.

## Slide 16: Future Scope
The Li-Fi technology is an advance approach on design, having the best design of internet by largely reducing the size of device which transfers data implementation by means of light bulbs.
The LED’s can provide feasible access.
Applications compared to any other networks in various fields which cannot be connected by on use networks.
Li-Fi has provided a step forward development in the world of growing hunger communication.
This technology is safe to all biodiversity including humans and progressing towards a greener, cheaper and brighter future of technologies.